## Slide 1: Raman data processing
Raman
spectrometer
output
SINGLE spectrum
.txt file
tageZ= MärzhauserX (µm)= 1012Y (µm)= 0Z (µm)= -14.9Project= Sample= Site= Title= 50nm_debondRemark= Date= 12.10.2018 15:15Acquired= 12.10.2018 15:15:09357.003 12.75
357.33 12.75
357.654 12.75
357.979 12.625
358.305 9.25
358.63 14
358.954 12.25
Header = 35 lines
2 data columns separated by \tab
Python parser and fitting script
Outputs\class attributes :
Peak position
FWHM
Offset
residue

## Slide 2: Python parser and fitting script
Packages imports
Raman_spectrum class definition (args : filename,wn_min=480, wn_max=560)
  Init function : extract raw data from .txt file
  Lorentzian : define lorentzian function for the fit
  Fit : fit value between wn_min and wn_max with a relentzian function, return parameter and residue
  Plot mehod (optional) : plot experimental data and fit on a same graph + save in output folder (optional)
  Force user input for force at which the specturm was measured
  Displacement : user input at which the spectrum was measured
  Time : extract time and store it as an attribute
Single spectrum

## Slide 3: Python parser and fitting script
Packages imports
Raman_spectrum class definition (args : filename,wn_min=480, wn_max=560)
  Init function : extract raw data from .txt file
  Lorentzian : define lorentzian function for the fit
  Fit : fit value between wn_min and wn_max with a relentzian function, return parameter and residue
  Plot mehod (optional) : plot experimental data and fit on a same graph + save ni output folder
  Force user input for force at which the specturm was measured
  Displacement : user input at which the spectrum was measured
  Time : extract time and store it as an attribute
xy_maps
File format :
34 lines header
35th line : wave number
0 and 1 columns are x and y coordinates in µm
500 501 501…
x1 y1 cts cts cts
x1 y2 cts cts…
…
x1 yN cts cts…
x2 y1 cts cts cts …
…..
xN yN cts cts cts …

## Slide 4: Tensile curve plot tool
Inputs :
  TDMS file or bulge height and radius in case of bulge test
  Raman files (prefix, range and folder)
  Sample dimension (for stress)
  Orientation [110] [100]
  Tensile configuration (uniaxial, biaxial)
Outputs
  Plot (eps\png) strain_si = f(strain_macro)
  .txt results
To use corresponding coefficient
Need to implement a GUI